Draft CR to change new B.30

Work status as of April 30

Impacted TSI: TAP TSI and TAF TSI

Headline: Change of B.30 (adding elements to receipt confirmation)

Type: Error correction

Documents and reference: Original document: B.30 following the alignment with TAF; changes according to TAF and TAP Phase 1 (WG5 & EG1 meetings)

Project information: adding functional elements to allow functional identification of earlier message

Problem/need: In the current Receipt Confirmation Messages, no information is given on the original request (train, path, request number) the receipt of which needs to be confirmed. Currently, only a related message number is confirmed. This number is however assigned by the Common Interface and not by the sending legacy system. The legacy system identifies the request by a functional identifier.

With the current Receipt Confirmation Message the original path request and/or concerned train cannot be identified. The typical example for the utilization of this message is the response of IM when Path Request of RU is received. The IM cannot provide a path offer (PathDetailsMessage) within a short amount of time, it can rather send a confirmation that the particular path request (with the particular path request data!) has been received.

Solution proposal by submitter: Therefore it is proposed to add the following elements to the message:

Identifiers (complex element)

TypeofRequest

TypeOfInformation

AffectedSection (complex element).

All elements are already in the message catalogue.

The new message is described in the annexed document.